## Slide 1: openDA_RRMDA_Themi - procedure
daemon (runs continuously)
  python batcher
    matlab getRaw_Themi
    matlab processRaw_Themi
    setup openDA run
    openDA oda_run.sh <file>.oda
      matlab runModel_Themi
    clean up openDA run
    matlab controlData_Themi
    matlab sendtoDB_Themi
    matlab MatlabMail_Themi

## Slide 2: i/o of runModel_Themi
runModel_Themi
restart/
E.mat
S0G0.mat
data/processed/sub/*
data/processed/db/
results/
forecast &
nowcast
python - setup openDA run:
copy content of restart/
data/processed/sub/*
Put it all to an openDA input directory
openDA run:
creates subdirectories for each model run by copying the content of the input directory. After the model run openDA summarizes all results in openDA result files. Use the restart option in openDA to avoid resampling of the ensemble every time openDA is started.
python - clean up openDA run:
Get results of current time step from the openDA run subdirectories
Reorganize them such that the normal RRMDA procedure can go on.

## Slide 3: openDA-runModel_Themi-wrappers
Detailed docu in the wrapper source code.
Ewrapper: read and write. must have.
S0G0wrapper: read and write. optional for stoch. initial states.
wrappers for sub-data: read. optional for stoch. bc. not implemented currently.
observation reader

## Slide 4: python set up method
Copy needed input files to input directory
Adapt restartInFile in RRMDA.oda file at each time step.

## Slide 5: clean up method, possibly call from within openDA
copy first replicate of E.mat from all openDA working directories to the original E.mat.